## Slide 1: Integrating physics-based depletion into fuel cycle simulation: When, how, and why
Steven E. Skutnik
University of Tennessee-Knoxville
2nd Technical Workshop on Fuel Cycle Simulation Columbia, SC

## Slide 2: Thermal-spectrum one-group cross-sections are highly sensitive to burnup & initial compositions
Initial enrichment
Average void fraction

## Slide 3: Reaction cross-sections show much higher sensitivity to perturbations in thermal energy region vs. fast

## Slide 4: Example: EG29 scenario
Fast spectrum: low CX sensitivity: Physics desirable, not “necessary”
Thermal spectrum: high CX sensitivity: CXs highly sensitive to (dynamic) initial Pu composition & burnup; physics necessary

## Slide 5: A tale of two MOXes
Chart: 
| Pu-239 | Pu-240 | Pu-242 | Pu-241 | Pu-238
24500 MWd/MTU | 59.0803 | 30.4504 | 4.215 | 5.2345 | 1.0195
Chart: 
| Pu-239 | Pu-240 | Pu-241 | Pu-242 | Pu-238
24500 MWd/MTU | 72.2016 | 19.8949 | 4.6818 | 2.4671 | 0.75451
Chart: 
| Pu-239 | Pu-240 | Pu-241 | Pu-242 | Pu-238
24500 MWd/MTU | 56.1538 | 26.1209 | 6.4402 | 8.3931 | 2.8914
W17x17 (PWR) 4.0 % enrichment
24.5
GWd/MTU
49.0
GWd/MTU
Depletion
MOX 17x17 (PWR)
8% Pu / NU 33 GWd/MTHM
1 MTHM basis
Chart: 
| Pu-239 | Pu-240 | Pu-242 | Pu-241 | Pu-238
49000 MWd/MTU | 46.592 | 33.563 | 10.9236 | 5.9247 | 2.9959
61.1 kgPu / iMT MOX
59.9 kgPu / iMT MOX

## Slide 6: Development and function of an Origen-based Reactor Analysis module (CyBORG)

## Slide 7: Introducing CyBORG: Cyclus-Based ORIGEN
Assimilating physics-based depletion into fuel cycle scenario development

## Slide 8: How do we incorporate ORIGEN into Cyclus?
Newest ORIGEN API facilitates direct, in-memory calls to ORIGEN solver
By developing a portable, embeddable “depletion engine,” ORIGEN operations can be “wrapped” into a Cyclus-friendly format
  “Depletion engine” builds from ORIGEN API (from shared SCALE/Origen libraries)
Notes: i.e., the “secret sauce” to developing an ORIGEN-based NFIM will be in the development of the standalone “depletion engine,” a portable set of “builder’s libraries” that encapsulate all of ORIGEN’s functions in a way that can be easily wrapped into Cyclus-facing calls
-To be portable, this will take the form of an embeddable library containing ORIGEN solver functionality OUTSIDE of SCALE – i.e., capturing all of the functionality inside a single, portable library
Note that this supports MORE than just depletion operations; provides for a general resource for physics-based operations (source terms: heat & activity, etc.); supports both general physics & other modules

## Slide 9: CyBORG provides physics-based flexibility for reactor simulations within Cyclus via coupling with Origen
C++ primitives only!
(no proprietary types)
Cyclus/Origen interface layer
CyBORG
Fuel cycle data
Input fuel recipe
Origen reactor data libraries
Output fuel recipe
Origen 6.2 API
Initial compositions
Powers
Problem-specific reactor data
Output compositions
Interpolable params
Assembly type
Cycle burnup(s)
Notes: Note that the Cyclus / Origen interface layer exposes only C++ primitives and standard library types, thereby effectively insulating Cyclus from Origen-specific types and vice versa.

## Slide 10: CyBORG balances the performance cost of depletion via a “hash-and-cache” recipe generation strategy†
Because of the relative cost of depletion (and reactor data library interpolation) relative to simulation time, we only to invoke physics-based depletion when necessary
Solution: Cache output recipe (generated via depletion) to a unique hash based on relevant depletion conditions
  e.g., initial enrichment, fuel type, discharge burnup
†Special thanks to Paul Wilson from UW-Madison for this idea

## Slide 11: Generalized reactor data interpolation and processing within CyBORG

## Slide 12: Accurate depletion calculations require problem-dependent nuclear data
Problem-specific nuclear data is required to dynamically produce accurate output inventories
  Flux spectrum evolves with initial enrichment, void, burnup, etc.
Origen handles this through interpolating pre-generated libraries to problem-specific conditions (e.g., initial enrichment, burnup, etc.)
  Libraries developed transport calculations
  “Assembly average” cross-sections

## Slide 13: Example dimensions for N-D interpolation
Initial composition
235U
239Pu : Pu
241Am
Void fraction
Temp. / power level
Burnup
Each parameter is treated as orthogonal, creating an N-dimensional interpolation (hyper-)space
Interpolation dimensions are unspecified until problem time (i.e., space is created dynamically)
N-D space collapsed to 1-D and then interpolated along burnup dimension for problem-specific burnups

## Slide 14: N-dimensional interpolation approach
(u´,v´)
Determine adjacent 1-D “knots” for each dimension
Determine independent weight factors for each dimension
Apply appropriate weights to cross-section data across each dimension
Notes: CHALLENGE here is to provide a GENERALIZED approach to interpolation across many dimensions which are unknown until run-time
C_i and C_j based on u’ and v’ only; idea is to calculate the relative “weights” in each independent dimension and then apply an independent interpolation across each dimension. Trying to touch “minimum” amount of data possible (for speed)
Amenable both to linear, lagrangian polynomial, and cubic spline type interpolation
Initial testing shows this appears to scale up to ORIGEN-sized datasets & anticipated interp dimensions reasonably well

## Slide 15: Conclusions

## Slide 16: Current status of CyBORG
CyBORG is designed to work with the latest SCALE 6.2.2 release
CyBORG v1.0 is now available for download and is fully compatible with Cyclus v1.5
CyBORG repository: https://github.com/sskutnik/cyborg

## Slide 17: Acknowledgements
This work has been funded by a Nuclear Energy University Programs (NEUP) grant sponsored by the U.S. Department of Energy, Office of Nuclear Energy, award number DE-NE0000737

## Slide 18: Questions?
sskutnik@utk.edu
https://github.com/sskutnik/cyborg